## Slide 1
ECE 220 Computer Systems & Programming
Lecture 2: Input/Output Abstractions
August 29, 2019
Notes: ECE Main Slide

## Slide 2: Outline
Section 8.1-8.4 of Patt and Patel
I/O principles
Input from keyboard
Output to monitor (reading assignment)
Key concepts
  Memory mapped I/O
  Asynchronous and synchronous communication

## Slide 3: Humanoid Robot

## Slide 4: I/O with the physical world
Sensors: cameras, RADARS, IMUs, Gyros
Actuators: servo motors, hydraulics, steering
CPU & Memory
Controlling bipedal gait,
Image processing, obstacle detecting, path planning, control, …
CPU and Memory
Control
Unit
PC, IR, FSM
Processing Unit
R0 … R7
ALU
Memory
Program
Data

## Slide 5: Complete system
Sensors: cameras, RADARS, IMUs, Gyros
Actuators: servo motors, hydraulics, steering
CPU & Memory
Controlling bipedal gait,
Image processing, obstacle detecting, path planning, control, …
CPU and Memory
Control
Unit
PC, IR, FSM
Processing Unit
R0 … R7
ALU
Memory
Program
Data
Many more examples
Autopilot
Antilock brakes
…
Autonomous cars
UAVs/Drones
Space rovers
Smart pacemakers
Powerplants
…

## Slide 6: I/O Layout
How to connect a keyboard to LC3?
  How to synchronize with the processor?
Interrupt I/O
Memory Mapped I/O
  Using existing instruction (LC3)
  Using IN/OUT separate instructions
Keyboard
LC-3

## Slide 7: how should we connect a keyboard to the computer?

## Slide 8: LC3 Memory: Memory mapped device registers
Address | Contents | Comments
x0000 |  | ;system space
… |  | 
x3000 |  | ; user space
 |  | ; programs
 |  | ; and data
… |  | 
xFE00 |  | ; Device registers maps
… |  | 
xFFFF |  | 
xFE00 KBSR
xFE02 KBDR
xFE04 DSR
xFE06 DDR
These are the memory addresses to which the device registers (KBDR, etc.) are mapped
The device registers physically are separate circuits from the memory

## Slide 9: P&P Appendix C Describes I/O Memory Mapping
(Patt and Patel Figure C.3)
Memory control signals are delivered to “address control logic.”

## Slide 10: Keyboard and Display are Memory-Mapped in LC-3
Based on MAR and these control signals, the address control logic controls:
  memory enable (chip select) signal actually delivered to the memory,
  load control for DDR,* and
  INMUX select lines, which determines whether memory, KBSR, KBDR, or DSR writes the load result to MDR.
*And for KBSR and DSR, but we’ll explain why later.

## Slide 11: Example: Reading the KBSR
(Patt and Patel Figure C.3)
read KBSR: MAR=xFE00, R.W=read MIO.EN=1
off

## Slide 12: Handshaking using KBDR and KBSR
When a char is typed by user in the keyboard
  Its ASCII code is placed in KBDR[0:7]
  KBSR[15] is set to 1 (ready bit)
  Keyboard is disabled, i.e., any further keypress is ignored
When KBDR is read by CPU
  KBSR[15] is set to 0
  Keyboard is enabled
This is part of the keyboard Hardware.

## Slide 13: Reading Input (first attempt)
START LDI R1, KBDRAdd ; Read from KBD
….
BRnzp START
KBDRAdd .FILL xFE02 ; Address of KBDR
KBDR
15
8
7
0
15
14
0
keyboard data
Does this work?

## Slide 14: Reading Input the right way
START LDI R1, KBSR_ADDR ; Test for
BRzp START ; character input
LDI R0, KBDR_ADDR
BRnzp NEXT_TASK ; Go to the next task
...
KBSR_ADDR .FILL xFE00 ; Address of KBSR
KBDR_ADDR .FILL xFE02 ; Address of KBDR
KBSR
KBDR
15
8
7
0
15
14
0
keyboard data
ready bit
This is how TRAP x20 = GETC works!

## Slide 15: I/O Layout
How to connect a display to LC3?
Display
LC-3

## Slide 16: Handshaking using DDR and DSR
When monitor is ready to display another char
  DSR[15] is set to 1: (ready bit)
When new char is written to DDR
  DSR[15] is set to 0
  Any other chars written to DDR are ignored
  DDR[7:0] is displayed
This is part of the display hardware.

## Slide 17: Example: Writing the DDR
(Patt and Patel Figure C.3)
write DDR: MAR=xFE06, R.W=write MIO.EN=1
off

## Slide 18: Writing TRAP x21
START LDI R1, DSR_ADDR ; Test for
BRzp START ; character input
STI R0, DDR_ADDR
BRnzp NEXT_TASK ; Go to the next task
...
DSR_ADDR .FILL xFE04 ; Address of DSR
DDR_ADDR .FILL xFE06 ; Address of DDR
DSR
DDR
15
8
7
0
15
14
0
output data
ready bit
This is how TRAP x21 = OUT works!

## Slide 19: Exercises
Write code for ECHO (read a char and display it)
Write code for PUTS (display a stored string)
Write a more sophisticated input function using command prompt.
Read Interrupt-driven I/O

## Slide 20: Summary of concepts
Memory mapped I/O (extra hardware for flexibility and convenience of programming)
Asynchrony
Polling