## Slide 1
ECE 220 Computer Systems & Programming
Lecture 4: Introduction to Stack Data Structures
September 5, 2019
Notes: ECE Main Slide

## Slide 2: Outline
What is a stack?
How to implement a stack?
POP and PUSH Subroutines in LC-3
Overflow and Underflow in stack
Chapter 10 in textbook

## Slide 3: The Stack Abstraction
Stack is an abstract data structure
Stack of books example:
  A new book always goes on top of the stack
  We can only remove a book from the top of the stack

## Slide 4: Palindromes:
Examples of palindromes
  Madam
  Kayak
  Was it a car or a cat I saw?
  Aibohphobia
How can we test for palindromes?

## Slide 5
Coin Holder Example
First coin in is the last coin out
5

## Slide 6
A Hardware Implementation
Data items move in memory, top of stack is fixed
6
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
Yes
Empty:
TOP
#18
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
No
Empty:
TOP
#18
#31
#5
#12
/ / / / / /
No
Empty:
TOP
#18
#31
/ / / / / /
/ / / / / /
/ / / / / /
No
Empty:
TOP
Initial State
After
One Push
After Three
More Pushes
After
Two Pops

## Slide 7
A Software Implementation
Data items don’t move in memory, just our idea about where the top of the stack is.
By convention, R6 holds the Top of Stack (TOS) pointer
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
/ / / / / /
/ / / / / /
/ / / / / /
#18
TOP
#12
#5
#31
#18
/ / / / / /
TOP
#12
#5
#31
#18
/ / / / / /
TOP
Initial State
After
One Push
After Three
More Pushes
After
Two Pops
x4000
x3FFF
x3FFC
x3FFE
R6
R6
R6
R6
x3FFF
x3FFE
x3FFD
x3FFC
x3FFB
/ / / / / /
7

## Slide 8: Why are Stack Data Structures useful?
Saving and Restoring of registers when we call a subroutine
  PUSH to save when we enter
  POP to restore when before we return
Stacks enable subroutines (and functions and methods) to be re-entrant*
  They can be interrupted
  They can call other subroutines, and have control return back to them, possibly recursively*
  Part of the foundation for multi-threading*
*These are big new concepts for many of you, and you’ll be exposed to them in more detail later in this course and in others

## Slide 9
Basic Push and Pop Code
Using Software Implementation of Stack
Push (R0 contains the data to be pushed)
  ADD R6, R6, #-1 ; decrement stack ptr
  STR R0, R6, #0 ; store data (to Top of Stack)
Pop (R0 contains the data after popped)
      LDR R0, R6, #0 ; load data from stack ptr
      ADD R6, R6, #1 ; increment stack ptr
What if we Push when the stack is full? Overflow
What if we Pop when the stack is empty? Underflow
x3FFF
x3FFE
x3FFD
x3FFC
x3FFB
#12
#5
#31
#18
/ / / / / /
TOP
8
Notes: Input: A B C
Output: B C A
Sequence: Push A, Push B, Pop B, Push C, Pop C, Pop A

## Slide 10: Our implementation
BASE: beginning of stack in memory (initial state)
MAX: end of stack in memory
START: Location of most recent element pushed (R6)
Address/Label | 
x3FFB | ;end of stack
… | 
x3FFF | ; Base of the stack
X4000 | ; start of stack
MAX | .FILL x3FFB
BASE | .FILL x4000
START | ….

## Slide 11: Overflow and Underflow
Given MAX, BASE, START, how do we determine…
Overflow?
Underflow?
Label/address | 
x3FEF | 
x3FFB | XXXXXXXXXXXX
… | XXXXXXXXXXXX
x3FFD | XXXXXXXXXXXX
x3FFE | XXXXXXXXXXXX
x3FFF | XXXXXXXXXXXX
x4000 | XXXXXXXXXXXX
MAX | .FILL x3FFB
BASE | .FILL x4000
START | …….
A Full Stack

## Slide 12: Figure 10.4 POP routine including the test for underflow

## Slide 13: Our implementation
BASE: beginning of stack in memory (initial state)
MAX: end of stack in memory
START: Location of most recent element pushed (R6)
Address/Label | 
x3FFB | ;end of stack
… | 
x3FFF | ; Base of the stack
X4000 | ; start of stack
MAX | .FILL x3FFB
BASE | .FILL x4000
START | ….

## Slide 14: Push 18
Address/Label | 
x3FFB | ;end of stack
… | 
x3FFF | 18
x4000 | 
MAX | .FILL x3FFB
BASE | .FILL x4000
START | x3FFF

## Slide 15: Push 31
Address/Label | 
x3FFB | ;end of stack
… | 
x3FFE | 31
x3FFF | 18
X4000 | 
MAX | .FILL x3FFB
BASE | .FILL x4000
START | x3FFE

## Slide 16: Push 5
Address/Label | 
x3FFB | ;end of stack
….. | 
x3FFD | 5
x3FFE | 31
x3FFF | 18
X4000 | 
MAX | .FILL x3FFB
BASE | .FILL x4000
START | x3FF3D

## Slide 17: Pop (return 5)
Address/Label | 
x3FFB | ;end of stack
….. | 
x3FFD | 5
x3FFE | 31
x3FFF | 18
X4000 | 
MAX | .FILL x3FFB
BASE | .FILL x4000
START | x3FF3E

## Slide 18: PUSH/POP implementation
BASE x4000
Top of the Stack – R6 (Stack Pointer)
Load – R0 (value to be popped)
Output – R5 (success / fail)
MAX x3FFB
Top of the Stack – R6 (Stack Pointer)
Store – R0 (value to be Pushed)
Output – R5 (success / fail)

## Slide 19: Exercise: > Push two values into the Stack > Pop those values from the stack > Add the poped Values and > put the result back into the stack